## Slide 1: Accelerating Training of DNNs via Sparse Edge Processing
Sourya Dey, Yinan Shao, Keith Chugg, Peter Beerel
ICANN, September 2017

## Slide 2: Overview of Current DNNs
Key machine learning technologies
Training done offline in CPU/GPU
Custom hardware used for inference only
Lot of parameters - Memory intensive
Slow to train - Computationally intensive

## Slide 3: Highlights of our Research
Predefined sparsity - Memory friendly
  30x less parameters in FC layers
Edge-based processing - Computationally flexible
Hardware optimizations - Fast training
  35x estimated speedup over GPUs
FPGA based architecture - Online training and inference
Krizhevsky, A., Sutskever, I., Hinton, G.E.: Imagenet classification with deep convolutional neural networks. In: NIPS-2012, pp. 1097–1105 (2012)

## Slide 4: Typical Supervised Network
Predictions
Convolutional Layers
Pooling and Normalization
Fully Connected Classifier
5% of total network connections
95% of total network connections
Krizhevsky, A., Sutskever, I., Hinton, G.E.: Imagenet classification with deep convolutional neural networks. In: NIPS-2012, pp. 1097–1105 (2012)
Zhang, C., Wu, D., Sun, J., Sun, G., Luo, G., Cong, J.: Energy-efficient CNN implementation on a deeply pipelined FPGA cluster. In: ISLPED-2016. pp. 326– 331. ACM, New York (2016)

## Slide 5: Focus of the Present Work
Predictions
Convolutional Layers
Pooling and Normalization
Fully Connected Classifier
95% of total network connections

## Slide 6: Sparsity
Sparsity – Predefined
Fully connected (FC) network
Sparse network
fo = 1, fi = 2
Connectivity = 25%
Fanout (fo) = 4
Connectivity = 100%
Fanin (fi) = 8

## Slide 7: Does predefined sparsity work?
3% connectivity gives >95% MNIST accuracy, within 3% of FC
Ongoing research shows:
Results can be further improved by planning connections
Trend holds for other datasets like CIFAR-10
Notes: These do NOT use CNNs or more hidden units, both of which can make this absolutely state-of-the-art, i.e. >99%

## Slide 8: Interleaving and Spread
0
1
2
3
4
5
6
7
I(0)
I(1)
I(2)
I(3)
I(4)
I(5)
I(6)
I(7)
0
1
2
3
4
5
6
7
I(0)
I(1)
I(2)
I(3)
I(4)
I(5)
I(6)
I(7)
Interleaver
Interleaver
Interleaver algorithm ensures:
Each output connected to a good chunk of different inputs
No neuron unconnected
Junction 1
Junction 2
I(0)
I(1)
I(2)
I(3)
I(4)
I(5)
I(6)
I(7)
I(0)
I(1)
I(2)
I(3)
I(4)
I(5)
I(6)
I(7)
Interleaver
Interleaver



## Slide 9: Edge Processing
Concurrent Network Processes
  Feedforward (FF) - Weights and activations
  Backpropagation (BP) - Weights, deltas and activation derivatives
  Parameter Update (UP) - Weights, deltas and activations
Weights (edges) used in all processes
  Single weight memory bank
Process z sets of parameters together
z = Degree of parallelism

## Slide 10: Memory Organization
z memories for all parameters
Read 1 entry from each memory at a time
Mem 1 | Mem 2 |  |  |  | Mem z
Mem 1 | Mem 2 |  |  |  | Mem z
Clash stalls processing 
Clash-free access 
Avoid clashes!

## Slide 11: Order of Accesses
Example: z=6
Natural order accesses for junction weights and next layer parameters
Permuted order accesses for previous layer parameters
Interleaver must prevent clashes

## Slide 12: Operational Parallelization in a Junction

## Slide 13: Pipelining across Junctions - Speedup

## Slide 14: Architecture Flexibility
Hardware Complexity, Area and Power
Processing Time
z increases
Changing z makes architecture automatically adapts to problem size and available hardware.
Suitable for FPGA reconfigurability
Notes: Big FPGAs or FPGA farms can support large z

## Slide 15: Hardware Simulations
fo=8
1024 Input
Neurons
64 Hidden
Neurons
fo=8
fi=128
Interleaver
Size = 8192
Interleaver
Size = 512
fi=32
16 Output
Neurons
z = 512
z = 32
Connectivity = 12.5%
Connectivity = 50%
Overall connectivity = 13%
Verilog RTL on MNIST dataset

## Slide 16: RTL Fixed Point Results vs Floating Point
3b integer +
7b fractional
Fixed point − Floating point
Total 100K
samples
Moving average of last 1000 samples

## Slide 17: Summary and Outstanding Issues
Flexible hardware architecture for online training and inference
Predefined sparsity reduces memory and computational complexity
Speedup due to operational parallelization and junction pipelining
Extend to other types of neural networks
Memory bandwidth bottlenecks
Theoretical exploration of connectivity patterns

## Slide 18
Thank you!
Questions?
Contact: souryade@usc.edu

## Slide 19: Performance Analysis of Sparsity
3% connectivity gives >95% accuracy in MNIST after 30 epochs, within 3% of FC
1.41% connectivity gives >80% accuracy in CIFAR10 after 5 epochs, within 2.5% of FC
Notes: PAB: As discussed, I think you can remove the CIFAR data as this was not on the paper.